Troubleshooting

| Logger does not switch on | make sure no cable is connected to the USB port make sure the batteries are charged if this does not work proceed with instructions below |
| --- | --- |
| Lock up: logger does not react on any user interaction | remove the elastic Velcro (pole mounting) with one screw at the back remove battery cover (screw on the bottom) remove the batteries for a few seconds insert batteries again, close cover and reattach Velcro restart logger |
| Logger beeps twice: general alert | On start-up screen: enter QNH to start logging. Read instructions on the screen. |
| Logger does not show a position | It might take a few minutes to get a GPS fix. Make sure the logger is mounted in an upright position and has clear visibility of the sky. |

Balloon Competition Logger

Quick Guide

Version 1.0

Switch On

- Press  to switch on logger
USB cable must not be connected at that time.

- Press to confirm

- Enter the QNH
Use the numbers from the task sheet.

- Your logger is ready

Idle Screen

| Satellites / Battery status |  |
| --- | --- |
| Position |  |
| Altitude (barometric) |  |
| Time (local) |  |
| Pilot ID, Logger S/N |  |
| Markers dropped |  |
| Goals declared |  |
| Soft keys Use first rows of keys to select |  |

Switch Off

- press  for 5 seconds

- press to confirm
It takes approx. 15 seconds to write the track file to the SD Card.

Drop a Marker

- Press  and select the marker number 
 -  to prepare the logger for marker drop.

- Your logger is on stand-by to drop the marker. 
It still shows your position in the lower part of the screen.

- Press to drop the marker or  to return to the idle screen.
The relevant icon on the idle screen turns to black background for confirmation.

Declare Goal

- Press  and select the goal  -  to prepare the logger for goal declaration.

- Enter your goal declaration (3 digits). Use arrows   to move cursor.

- Enter altitude if needed or press

- Press to save declaration or  to return to the idle screen.
The relevant icon on the idle screen turns to black background for confirmation.
You can only cancel if the cursor is not in one of the text fields. Use  until the background of  turns black then press

# Text boxes

Sensitive area

Sensitive area